## Slide 1: Τηλεπικοινωνιακά Δίκτυα
ΠΜΣ Μηχανικών Ηλεκτρονικών Υπολογιστών και Δικτύων
Τμήμα Πληροφορικής & Τηλεπικοινωνιών – Πανεπιστήμιο Ιωαννίνων
Διδάσκοντες
Κωνσταντίνος Αγγέλης
Καθηγητής
Ανδρέας Τσορμπατζόγλου
Επίκουρος Καθηγητής

## Slide 2: Τηλεπικοινωνιακά Δίκτυα
Βασικές αρχές μετάδοσης
Δίκτυα επικοινωνιών
Τεχνολογία ασύρματης επικοινωνίας
Το ασύρματο κανάλι
Ορθογωνική πολυπλεξία διαίρεσης συχνότητας
Διασπορά φάσματος
Αρχές Διάδοσης Σημάτων - Κυψελοειδή ασύρματα δίκτυα
Συστήματα 4ης-5ης γενιάς και LTE-Advanced
Συστήματα MIMO
Επικοινωνίες μεγάλης εμβέλειας
Συνεργατικά Τηλεπικοινωνιακά Συστήματα
Οπτικά Δίκτυα
ΠΜΣ Μηχανικών Ηλεκτρονικών Υπολογιστών και Δικτύων
Τμήμα Πληροφορικής & Τηλεπικοινωνιών – Πανεπιστήμιο Ιωαννίνων

## Slide 3: Σύγχρονα ασύρματα δίκτυα
Οι τεχνολογίες MIMO & OFDM σε συνδυασμό αποτελούν τον ακρογωνιαίο λίθο στα αναδυόμενα ευρυζωνικά ασύρματα δίκτυα
OFDM  Τεχνική Βασιζόμενη στο Διαφορισμό

## Slide 4: Τεχνικές Διαφορισμού (Diversity Techniques)
Ο Διαφορισμός (Diversity) βασίζεται στο γεγονός ότι ανεξάρτητα κανάλια υφίστανται ανεξάρτητα φαινόμενα διαλείψεων
Space diversity – techniques involving physical transmission path, spacing antennas
Frequency diversity – techniques where the signal is spread out over a larger frequency bandwidth or carried on multiple frequency carriers
Time diversity – techniques aimed at spreading the data out over time
Use of diversity
  Selection diversity – select the best signal
  Combining diversity – combine the signals

## Slide 5: MULTIPLE INPUT MULTIPLE OUTPUT (MIMO) ANTENNAS
Use antenna arrays for
  Diversity (Διαφορισμός) – different signals from different antennas
  Multiple streams– parallel data streams
  Beamforming (Μορφοποίηση Δέσμης) – directional antennas
  Multi-user MIMO – directional beams to multiple simultaneous users
Modern systems
  4 × 4 (4 transmitter and 4 reciever antennas)
  8 × 8
  Two dimensional arrays of 64 antennas
  Massive MIMO with many more antennas

## Slide 6: 5.9 Four Uses of MIMO

## Slide 7: Διασπορά Φάσματος και OFDM
Frequency diversity examples:
Ορθογωνική Πολυπλεξία Διαίρεσης Συχνότητας (Orthogonal Frequency Division Multiplexing - OFDM)
Διασπορά Φάσματος (Bandwidth expansion or Spread Spectrum)

## Slide 9: Orthogonal Frequency Division Multiplexing (OFDM)

## Slide 10: Ορθογωνική πολυπλεξία διαίρεσης συχνότητας Orthogonal Frequency Division Multiplexing (OFDM) Εισαγωγικά
OFDM created great expansion in wireless networks
  Greater efficiency in bps/Hz
Main air interface in the change from 3G to 4G
  Also expanded 802.11 rates
Critical technology for broadband wireless access
  WiMAX

## Slide 11: 8.1 Ορθογωνική πολυπλεξία διαίρεσης συχνότητας
Also called multicarrier modulation (Διαμόρφωση πολλαπλής φέρουσας)
Start with a data stream of R bps
  Could be sent with bandwidth Nfb
  With bit duration 1/R
OFDM splits into N parallel data streams
  Called subcarriers
  Each with bandwidth fb
  And data rate R/N (bit time N/R)

## Slide 12: Figure 8.1 Conceptual Understanding of Orthogonal Frequency Division Multiplexing

## Slide 13: Ορθογωνικότητα - Orthogonality
The spacing of the fb frequencies allows tight packing of signals
  Actually, with overlap between the signals
  Signals at spacing of fb ,2fb, 3fb ,etc.
The choice of fb is related to the bit rate to make the signals orthogonal
  Average over bit time of s1(t) × s2(t) = 0
  Receiver is able to extract only the s1(t) signal
    If there is no corruption in the frequency spacing
Traditional FDM makes signals completely avoid frequency overlap
  OFDM allows overlap which greatly increases capacity

## Slide 14: Figure 8.2 Illustration of Orthogonality of OFDM

## Slide 15: Ορθογωνικότητα - Orthogonality
Given an OFDM subcarrier bit time of T
  fb must be a multiple of 1/T
Example: IEEE 802.11n wireless LAN
  20 MHz total bandwidth
    Only 15 MHz can be used
  48 subcarriers
  fb = 0.3125 MHz
  Signal is translated to 2.4 GHz or 5 GHz bands

## Slide 16: Οφέλη της τεχνικής OFDM - Benefits of OFDM
Frequency selective fading only affects some subcarriers
  Can easily be handled with a forward error-correcting code
More importantly, OFDM overcomes intersymbol interference (ISI)
  ISI is a caused by multipath signals arriving in later bits
  OFDM bit times are much, much longer (by a factor of N)
    ISI is dramatically reduced
  N is chosen so the root-mean-square delay spread is significantly smaller than the OFDM bit time
  It may not be necessary to deploy equalizers to overcome ISI
    Eliminates the use of these complex and expensive devices.

## Slide 17: Υλοποίηση της τεχνικής OFDM - OFDM Implementation
Inverse Fast Fourier Transform (IFFT)
  The OFDM concept (Figure 8.1) would use N oscillators for N different subcarrier frequencies
    Expensive for transmitter and receiver
  Discrete Fourier Transform (DFT) processes digital signals
    If N is a power of two, the computational speed dramatically improves by using the fast version of the DFT (FFT).
  Transmitter takes a symbol from each subcarrier
    Makes an OFDM symbol
    Uses the Inverse FFT to compute the data stream to be transmitted
    OFDM symbol provides the weights for each subcarrier
    Then it is sent on the carrier using only one oscillator

## Slide 18: Figure 8.3 IFFT Implementation of OFDM

## Slide 19: Κυκλικό Πρόθεμα - Cyclic prefix
OFDM’s long bit times eliminate most of the ISI
OFDM also uses a cyclic prefix (CP) to overcome the residual ISI
  Adds additional time to the OFDM symbol before the real data is sent
    Called the guard interval
    ISI diminishes before the data starts
  Data from the end of the OFDM symbol is used as the CP
    Simplifies the computations

## Slide 20: Figure 8.4 Cyclic Prefix
Ονομαστικό κυκλικό πρόθεμα: 7% &
Εκτεταμένο κυκλικό πρόθεμα: 25% επιπλέον σύμβολα.
π.χ.: OFDM με 1024 υποφέρουσες με χρήση Ονομαστικού κυκλικού προθέματος έχει επιπλέον 0.07*1024=72 σύμβολα φύλαξης

## Slide 21: Δυσκολίες υλοποίησης της OFDM - Difficulties of OFDM
Peak-to-average power ratio (PAPR) (Λόγος Μέγιστης προς Μέση Ισχύ)
  For OFDM signals, this ratio is much higher than for single-carrier signals
  OFDM signal is a sum of many subcarrier signals
    Total can be very high or very low
Power amplifiers need to amplify all amplitudes equally
  Should have a linear characteristic with slope K on a Vout vs. Vin curve
  Yet practical amplifiers have limited linear ranges
    Causing distortion if outside the linear range

## Slide 22: Figure 8.5 Ideal and Practical Amplifier Characteristics

## Slide 23: Figure 8.6 Examples of Linear and Nonlinear Amplifier Output

## Slide 24
PAPR problem (continued)
  Expensive amplifiers have wide linear range
Solutions
  Could reduce the peak amplitude
    Called input backoff
    But this would increase the signal to interference plus noise ratio (SINR)
      Noise and interference would be relatively stronger because signal is weaker
  Specific PAPR reduction techniques can be used
    Specialized coding, phase adjustments, clipping, etc.
    Single-carrier FDMA (SC-FDMA)
Δυσκολίες υλοποίησης της OFDM - Difficulties of OFDM

## Slide 25
Intercarrier Interference (ICI) (Διαφεροντική Παρεμβολή)
  OFDM frequencies are spaced very precisely
  Channel impairments can corrupt this
  Cyclic prefix helps reduce ICI
    But CP time should be limited so as to improve spectral efficiency
    A certain level of ICI may be tolerated to have smaller CPs
  Doppler spread, mismatched oscillators, or even one subcarrier can cause ICI
    Spacing between subcarriers may need to be increased
    Could also use different pulse shapes, self-interference cancellation, or frequency domain equalizers.
Δυσκολίες υλοποίησης της OFDM - Difficulties of OFDM

## Slide 26: Πολλαπλή πρόσβαση με Ορθογωνική διαίρεση συχνότητας - OFDMA
Orthogonal Frequency Division Multiple Access (OFDMA) uses OFDM to share the wireless channel
  Different users can have different slices of time and different groups of subcarriers
  Subcarriers are allocated in groups
    Called subchannels or resource blocks
    Too much computation to allocate every subcarrier separately

## Slide 27: Figure 8.7 OFDM and OFDMA

## Slide 28: Πολλαπλή πρόσβαση με Ορθογωνική διαίρεση συχνότητας - OFDMA
Subchannel allocation
  Adjacent subcarriers (Παρακείμενες υποφέρουσες) – similar SINR
    Must measure to find the best subchannel
  Regularly spaced subcarriers (Υποφέρουσες σε τακτικές αποστάσεις) – diverse SINR
  Randomly space subcarriers (Υποφέρουσες σε τυχαίες αποστάσεις) – diverse SINR and reduced adjacent-cell interference

## Slide 29: Ευκαιριακός χρονοπρογραμματισμός - Opportunistic scheduling
Schedule subchannels and power levels based on
  Channel conditions
  Data requirements
Adjust in a dynamic fashion
  Use channel variations as an opportunity to schedule the best choice in users
    Hence the term opportunistic scheduling
  Criteria (maybe more than one used simultaneously)
    System efficiency (αποδοτικότητα) – pick users with best throughput (ρυθμοαπόδοση)
    Fairness (αμεροληψία) – proportional fairness considers the ratio of users’ current rates to the users’ average rates to know when a channel is best for them
    Requirements – audio, video
    Priority – public safety, emergency, or priority customers

## Slide 30: 8.3 FDMA απλής φέρουσας – (SC-FDMA)
SC-FDMA has similar structure and performance to OFDMA
  But lower PAPR
  Mobile user benefits – battery life, power efficiency, lower cost
  Good for uplinks
Uses extra DFT operation and frequency equalization compared to OFDM
  DFT prior to IFFT
  Spreads data symbols over all subcarriers
  Every data symbol is carried by every subcarrier
Multiple access is not possible
  At one time, all subcarriers must be dedicated to one user
  Multiple access is provided by using different time slots

## Slide 31: Figure 8.8 Simplified Block Diagram of OFDMA and SC-FDMA

## Slide 32: Figure 8.9 Example of OFDMA and SC-FDMA