## Slide 1: Τηλεπικοινωνιακά Δίκτυα
ΠΜΣ Μηχανικών Ηλεκτρονικών Υπολογιστών και Δικτύων
Τμήμα Πληροφορικής & Τηλεπικοινωνιών – Πανεπιστήμιο Ιωαννίνων
Διδάσκοντες
Κωνσταντίνος Αγγέλης
Καθηγητής
Ανδρέας Τσορμπατζόγλου
Επίκουρος Καθηγητής

## Slide 2: Διασπορά Φάσματος (Spread Spectrum)
Input is fed into a channel encoder
  Produces analog signal with narrow bandwidth
Signal is further modulated using sequence of digits
  Spreading code or spreading sequence
  Generated by pseudonoise, or pseudo-random number generator
Effect of modulation is to increase bandwidth of signal to be transmitted

## Slide 3: 9.1 General Model of Spread Spectrum Digital Communication System

## Slide 4: Spread Spectrum
On receiving end, digital sequence is used to demodulate the spread spectrum signal
Signal is fed into a channel decoder to recover data

## Slide 5: Spread Spectrum
What can be gained from apparent waste of spectrum?
  Immunity from various kinds of noise and multipath distortion
  Can be used for hiding and encrypting signals
  Several users can independently use the same higher bandwidth with very little interference

## Slide 6: Frequency Hoping Spread Spectrum (FHSS)
Signal is broadcast over seemingly random series of radio frequencies
  A number of channels allocated for the FH signal
  Width of each channel corresponds to bandwidth of input signal
Signal hops from frequency to frequency at fixed intervals
  Transmitter operates in one channel at a time
  Bits are transmitted using some encoding scheme
  At each successive interval, a new carrier frequency is selected

## Slide 7: 9.2 Frequency Hopping Example

## Slide 8: 9.3 Frequency Hopping Spread Spectrum System

## Slide 9: Frequency Hoping Spread Spectrum
Channel sequence dictated by spreading code
Receiver, hopping between frequencies in synchronization with transmitter, picks up message
Advantages
  Eavesdroppers hear only unintelligible blips
  Attempts to jam signal on one frequency succeed only at knocking out a few bits

## Slide 10: FHSS Using MFSK
MFSK signal is translated to a new frequency every Tc seconds by modulating the MFSK signal with the FHSS carrier signal
For data rate of R:
  duration of a bit: T = 1/R seconds
  duration of signal element: Ts = LT seconds
Tc ≥ Ts - slow-frequency-hop spread spectrum
Tc < Ts - fast-frequency-hop spread spectrum

## Slide 11: 9.4 Slow-Frequency-Hop Spread Spectrum Using MFSK 1M = 4, k = 22

## Slide 12: 9.5 Frequency-Hop Spread Spectrum Using MFSK 1M = 4, k = 22

## Slide 13: FHSS Performance Considerations
Large number of frequencies used
Results in a system that is quite resistant to jamming
  Jammer must jam all frequencies
  With fixed power, this reduces the jamming power in any one frequency band

## Slide 14: Direct Sequence Spread Spectrum (DSSS)
Each bit in original signal is represented by multiple bits in the transmitted signal
Spreading code spreads signal across a wider frequency band
  Spread is in direct proportion to number of bits used
One technique combines digital information stream with the spreading code bit stream using exclusive-OR (Figure 9.6)

## Slide 15: 9.6 Example of Direct Sequence Spread Spectrum

## Slide 16: 9.7 Direct Sequence Spread Spectrum System

## Slide 17: DSSS Using BPSK
Multiply BPSK signal,
  sd(t) = A d(t) cos(2π fct)
by c(t) [takes values +1, -1] to get
  s(t) = A d(t)c(t) cos(2π fct)
    A = amplitude of signal
    fc = carrier frequency
    d(t) = discrete function [+1, -1]
At receiver, incoming signal multiplied by c(t)
  Since, c(t) x c(t) = 1, incoming signal is recovered

## Slide 18: 9.8 Example of Direct Sequence Spread Spectrum Using BPSK

## Slide 19: 9.9 Approximate Spectrum of Direct Sequence Spread Spectrum Signal

## Slide 20: Code-Division Multiple Access (CDMA)
Basic Principles of CDMA
  D = rate of data signal
  Break each bit into k chips
    Chips are a user-specific fixed pattern
  Chip data rate of new channel = kD

## Slide 21: CDMA Example
If k=6 and code is a sequence of 1s and -1s
  For a ‘1’ bit, A sends code as chip pattern
    <c1, c2, c3, c4, c5, c6>
  For a ‘0’ bit, A sends complement of code
    <-c1, -c2, -c3, -c4, -c5, -c6>
Receiver knows sender’s code and performs electronic decode function
    <d1, d2, d3, d4, d5, d6> = received chip pattern
    <c1, c2, c3, c4, c5, c6> = sender’s code

## Slide 22: 9.10 CDMA Example

## Slide 23: CDMA Example
User A code = <1, –1, –1, 1, –1, 1>
  To send a 1 bit = <1, –1, –1, 1, –1, 1>
  To send a 0 bit = <–1, 1, 1, –1, 1, –1>
User B code = <1, 1, –1, – 1, 1, 1>
  To send a 1 bit = <1, 1, –1, –1, 1, 1>
Receiver receiving with A’s code
  (A’s code) x (received chip pattern)
    User A ‘1’ bit: 6 -> 1
    User A ‘0’ bit: -6 -> 0
    User B ‘1’ bit: 0 -> unwanted signal ignored

## Slide 24: 9.11 CDMA in a DSSS Environment

## Slide 25: Rake receiver
RAKE receiver
  Multiple versions of a signal arrive more than one chip interval apart
  RAKE receiver attempts to recover signals from multiple paths and combine them
This method achieves better performance than simply recovering dominant signal and treating remaining signals as noise

## Slide 26: 9.12 Principle of RAKE Receiver

## Slide 27: Categories of Spreading Sequences
Spreading Sequence Categories
  PN sequences
  Orthogonal codes
For FHSS systems
  PN sequences most common
For DSSS systems not employing CDMA
  PN sequences most common
For DSSS CDMA systems
  PN sequences
  Orthogonal codes

## Slide 28: PN Sequences
PN generator produces periodic sequence that appears to be random
PN Sequences
  Generated by an algorithm using initial seed
  Sequence isn’t statistically random but will pass many test of randomness
  Sequences referred to as pseudorandom numbers or pseudonoise sequences
  Unless algorithm and seed are known, the sequence is impractical to predict